## Slide 1: Six-Legged Walker: Brains with Their Own Rhythm
ECE497 Evolutionary Robotics ·
(Optional idea for a Project)

## Slide 2: Every brain so far has been a function
Projects 3–4
Feedforward network
Output depends only on the current input
No memory: same input, same output
Project 5
Feedforward + a clock
Rhythm handed in from outside, as sin and cos inputs
The brain only shapes it
Optional Project
CTRNN
Internal state that changes in time
Makes its own rhythm, even with no input
Walking is rhythmic. Insects walk using central pattern generators: circuits of neurons that produce a rhythm on their own. Can evolution build one?

## Slide 3: The task: make six legs walk
An evolved CTRNN walking, seen from above, head to the right. Red dots: feet down.
Six legs; each one swings forward and back, and puts its foot down or lifts it
A planted foot pushes the body; a lifted one swings back into place
The body only moves while the planted feet hold it up: a stable tripod
Fitness: average forward speed
Nobody tells it how to walk. Evolution has to find a leg-timing pattern, and a brain that produces it

## Slide 4: The CTRNN
A neural network that is a dynamical system
1
2
3

## Slide 5: One neuron, one equation
τi dyi/dt = −yi + Σj wji oj + Ii oi = σ(yi + θi)
y
state
The neuron's internal activity. This is what carries over from one moment to the next.
τ
time constant
How fast the state responds. Bigger τ, slower neuron.
−y
leak
With no input, the state decays back toward 0.
Σ w o
recurrent input
Weighted outputs of every neuron, including itself. w can be + or −.
θ
bias
Shifts where the neuron turns on.
o = σ(·)
output
Sigmoid of state + bias: always between 0 and 1. I is an external input, e.g. a sensor.

## Slide 6: What the bias and the time constant do
θ moves the sigmoid left or right: a neuron with a large bias is on almost no matter what, a very negative one is off.
τ sets the speed: the same input, switched on at t = 0, reaches the same value, sooner or later.

## Slide 7: Neurons talk to each other, in loops
1
2
3
Any neuron can connect to any other, and to itself
Feedforward: activity flows one way, through each layer once. Same input, same output.
Recurrent: activity keeps circulating. What the network does now depends on what it was doing a moment ago.
That's what lets it remember, and make its own rhythm.
In the code
Weights[j][i] = connection from neuron j to neuron i
Input to every neuron at once:
Weights.T @ Outputs

## Slide 8: Simulating it: tiny steps forward in time
def step(self, dt):
netinput = self.Inputs + np.dot(self.Weights.T, self.Outputs)
self.States += dt * (self.invTimeConstants
* (-self.States + netinput))
self.Outputs = sigmoid(self.States + self.Biases)
Euler integration: y ← y + dt · dy/dt
Compute how fast every state is changing right now, take a small step in that direction, repeat
dt must be small compared to the smallest τ. Too big, and the simulation is wrong; bigger still (dt > 2τ) and it blows up
Unit 6: τ ≥ 0.1, dt = 0.01. Project 6: τ ≥ 1, dt = 0.1
The exact answer rises smoothly to 1. With bigger steps it overshoots; at dt = 2.2 it diverges.

## Slide 9: Unit 6: a CTRNN in 60 lines of NumPy
import ctrnn
nn = ctrnn.CTRNN(3) # 3 neurons
nn.randomizeParameters() # random w, θ, τ
nn.setCenterCrossing() # optional (later)
nn.initializeState(np.random.uniform(-1, 1, 3))
for t in range(steps):
nn.step(dt)
outputs[t] = nn.Outputs
ctrnn.py
The network: states, weights, biases, time constants, step(dt)
sim.py
Simulate one circuit; plot each neuron over time, and neuron 1 vs. neuron 2
exp.py
Simulate hundreds of circuits; count how many oscillate
PythonBasics/Unit6: the same pieces as Project 6's controller, with nothing else attached. No body, no inputs: just the dynamics.

## Slide 10: With no inputs at all, a CTRNN can...
Settle down
All activity dies into a fixed point and stays there. The most common outcome for a random circuit.
Oscillate
Activity repeats forever, with its own period: a rhythm nobody put in from outside.
They can also switch between several resting states, or behave chaotically. Which you get depends on the parameters, and sometimes on where you start.

## Slide 11: A two-neuron oscillator
1
2
−1
+1
2 turns 1 on; 1 turns 2 off; 2 off lets 1 fall; 1 off lets 2 rise... Each neuron excites itself (+4.5), so it tends to stay on or off; the cross connections keep pushing them over the edge. In output space the trajectory ends in a loop: a limit cycle.
sim.py with circuit = "oscillator" (θ = −2.75, −1.75; τ = 1)

## Slide 12: Center-crossing: put every neuron where it's sensitive
Random weights and biases push most neurons fully on or fully off. A saturated neuron ignores its inputs, so activity freezes
A neuron's input from the others always lies between the sum of its negative weights and the sum of its positive ones
Center-crossing: set each bias so the middle of that range lands on the steepest part of the sigmoid
θi = −Σj wji / 2
nn.setCenterCrossing() Mathayomchan & Beer (2002)

## Slide 13: Same weights and time constants, different biases
# sim.py
size = 3
seed = 3
circuit = "random"
# or "centercrossing"
Same seed: same weights and time constants, only the biases change
Random: neuron 2 is pinned at 0, the others freeze within a few time units
Center-crossing: all three neurons cycle, forever

## Slide 14: How common is rhythm?
exp.py
100 random circuits per size, each with random and with center-crossing biases
Throw away the first 100 time units; count it as rhythmic if a neuron keeps swinging (2+ full cycles)
Random: 0–4%. Center-crossing: up to 37%, and more with more neurons
Why does one neuron never oscillate?
About 1 minute. Change sizes, samples, or the parameter ranges, and run it again.

## Slide 15: Try it: Unit 6
# sim.py: change these, run it again
size = 3
duration = 100.0
dt = 0.01
circuit = "random"
seed = None
python3 sim.py
python3 exp.py
Seed 3: random vs. center-crossing, same weights
Oscillator: what changes if you flip the sign of one cross connection?
dt: make it bigger until the plots change. When, and why?
Size: what do 10 center-crossing neurons do?
Duration: some circuits take a long time to settle. How long is long enough?
Output space: a point, a loop, or a tangle?

## Slide 16: From Unit 6 to the walker
Same equations, now wired to a body
L1
L2
L3
R3
R2
R1

## Slide 17: The walker body
L1
L2
L3
R3
R2
R1
Top-down; head to the right. Orange: foot down (L1, R2, L3: a tripod)
Senses: each leg's angle (6 numbers)
Acts: forward, backward, and foot for each leg (18 numbers in [0, 1])
foot > 0.5: planted. A planted leg pushes the body; a lifted leg swings
Balance: the body moves only while the planted feet hold it up: 3 or more, on both sides, around its center
Fitness: average forward speed, at most 1.0

## Slide 18: Things to know about the simulator
0.1 s
per tick. One CTRNN step per tick of the body (dt = 0.1)
220 s
per episode: 2,200 ticks, each from random starting leg angles
3
episodes averaged for every fitness evaluation
1.0
maximum speed. Fitness near 0: the body never got off the ground
Setup: a fresh virtual environment, then pip install -r requirements.txt
NumPy, Matplotlib, PyTorch, EvoTorch; plus Gymnasium and MuJoCo for the optional part. No special Python version this time.
The physics is idealized: no mass, friction or contact forces. That's what makes it fast, and what the optional MuJoCo part is about.

## Slide 19: Same CTRNN, wired to a body
Unit 6
CTRNN.step(dt)
netinput = Inputs + W.T @ Outputs
States += dt/τ * (-States + netinput)
Outputs = sigmoid(States + Biases)
Project 6
WalkerCTRNNController.act(observation)
inputs = WS * angle[leg] # sensors in
netinput = inputs + W.T @ Outputs
States += dt/τ * (-States + netinput)
Outputs = sigmoid(States + Biases)
return Outputs[command_idx] # 18 actions out
18 command neurons: forward, backward, and foot for each leg. Their outputs are the actions
Sensors: each command neuron hears its own leg's angle, through an evolved weight WS
The genome: numbers in [0, 1], decoded to weights and biases in [−16, 16] and time constants in [1, 20]
reset_state() randomizes the states at the start of every episode; act() is one Euler step

## Slide 20: One leg circuit, copied six times
L1
L2
L3
R3
R2
R1
■ across the body (CBW) ■ along each side (ISW) ● fwd, bwd ● foot
Every leg runs the same 3-neuron circuit (same weights): like an insect's segmental ganglia
A few connections between neighboring legs, also shared
24 genes build an 18-neuron network
Genome (module size 3)
W
WS
CBW
ISW
τ
θ
--module_size adds free interneurons to every leg's circuit

## Slide 21: Or one big network: choosing a topology
--topology | Settings | Neurons | Genome | Weight sharing
modular | --module_size 3 (default) | 18 | 24 | yes
modular | --module_size 5 | 30 | 50 | yes
modular | --module_size 8 | 48 | 104 | yes
fully_connected | --interneurons 0 | 18 | 378 | no
fully_connected | --interneurons 6 | 24 | 642 | no
Fully connected: every connection is its own gene. Nothing is assumed about legs or symmetry, and the genome is 16× bigger
Bigger isn't free: more genes, same budget of evaluations

## Slide 22: Where does the rhythm come from?
--mode cpg
Central pattern generator
brain
body
Sensors off. The rhythm has to come from the circuit alone.
--mode rpg
Reflexive pattern generator
brain
body
Sensors on (default). The rhythm can come from the circuit, the body, or both.
--mode mpg
Mixed
brain
body
Episodes alternate between sensors off and on. Fitness is the average: it has to walk either way.
Beer & Gallagher (1992). Try a walker in the mode it wasn't evolved in: sim.py --mode cpg

## Slide 23: Center-crossing, in the walker
--center_crossing seeds the first generation with center-crossing biases (including the sensory and inter-leg weights)
Only the starting population: evolution can move the biases anywhere afterward
Center-crossing walked in 3 of 3 runs. Random biases got stuck skating in 2 of 3
But the fastest walker of all (0.92) came from random biases
Three runs is an anecdote, not an answer. How would you find out?

## Slide 24: Evolving it
Running, watching, and reading what evolution built

## Slide 25: Running it
# evolve a CTRNN (about 3 minutes on a 16-core laptop)
python evolve.py --controller ctrnn --center_crossing --seed 1 --verbose --vizperf \
--output walker.npy --fitness_output walker_fit.npz
# score it; then again with its sensors cut
python sim.py --controller ctrnn --genome walker.npy --scores
python sim.py --controller ctrnn --genome walker.npy --mode cpg --scores
# gait diagram, neuron outputs, and an animation
python sim.py --controller ctrnn --genome walker.npy --trace walk.dat
python visualize_walker.py walk.dat --out_prefix walk --topology modular --module_size 3
Pass sim.py the same controller settings you evolved with. --algorithm es swaps the GA for CMA-ES.
Save --output and --fitness_output for every run you might want to plot later.

## Slide 26: Reading a gait diagram
One row per leg. Black: foot down. White: swinging
Bottom: body speed. It drops to 0 whenever the planted feet stop holding it up
Look for the pattern: one or two legs lifted at a time, in a repeating order: a slow wave-like gait, not a tripod. It stumbles twice before it settles in

## Slide 27: Inside the circuit
Every neuron's output over time, one row per leg: forward, backward, foot
Which neurons oscillate? Which just follow along?
Same circuit on every leg, but different timing: where do the phase differences come from?
Cut the sensors, remove a neuron, freeze an output: what breaks?

## Slide 28: Two walkers, two sources of rhythm
The walker evolved with its sensors off (cpg, center-crossing): a steady rhythm, never stalls
Evolved in | Sensors on | Sensors off
rpg | 0.77 | 0.04
cpg | 0.03 | 0.61
Average speed, 5 episodes, run under each condition
Each walker only works the way it evolved
The rpg walker needs its sensors: its rhythm runs through the body
The cpg walker makes its own rhythm, and live sensory input throws it off
Could one walker do both? --mode mpg

## Slide 29: Watch out: walking vs. skating
Fitness 0.07, and it plateaued there
All six feet down, pushing: the body glides forward
Until the feet are dragged too far behind, and it's stuck for good
Easy to find, better than standing still, a dead end
A fitness number tells you how far, not how. Look at the gait.

## Slide 30: How long it takes
3 min
per run on a 16-core laptop (50 genomes × 100 generations)
15,000
episodes per run: 50 × 100 × 3, each 2,200 ticks of physics
0
GPUs needed: the cost is the physics loop, spread across CPU cores
Time a short run on your own machine first: --popsize 20 --gens 20
Fewer cores, proportionally longer. Start early, and let runs work while you analyze others
Evolution is stochastic: one run is an anecdote. Use --seed, and several seeds before you trust a conclusion

## Slide 31: Optional: real physics
Does a walker evolved here walk in MuJoCo?

## Slide 32: Same genome, more realistic physics
The walker from the previous slides, on the MuJoCo hexapod: it stays upright, but moves only about 1.2 units in 50 s.
 | walker.py | hexapod (MuJoCo)
Physics | idealized | mass, friction, contact
Senses | 6 leg angles | 35 values
Acts | 18 values in [0, 1] | 12 torques: sweep, lift
Time step | 0.1 s | 0.05 s
hexapod_bridge.py: sweep torque = forward − backward; foot sets a target lift angle
--timescale (CTRNN speed vs. body) and --lift_gain matter, and interact
Expect it to fail at first. That gap is the challenge

## Slide 33: The assignment
The most open-ended project yet
P1
P2
P3
P4
P5
P6
how much is up to you

## Slide 34: Two required parts, one optional
Required 1
Evolve a CTRNN that walks
Really walks: stepping, not skating
Show it: fitness, gait diagram, animation
Explain how it walks: what are the neurons doing? Where does the rhythm come from?
Required 2
An experiment of your own
Ask a question about this world
Predict, vary one thing, enough seeds
What did you learn?
Optional · +1 extra credit
Walk in MuJoCo
Transfer a walker to the realistic body
Close the gap any way you like
A careful attempt counts, even if it never walks
Any settings, any topology, any mode. Say what you chose, and why.
Checkpoint: TBA (Part 1, demo) Report due: TBA Presentations: TBA

## Slide 35: Ideas for your experiment
A
Where's the rhythm?
cpg vs. rpg vs. mpg. Cut a walker's sensors
B
Inside the circuit
Lesion neurons or connections. Does one leg oscillate alone?
C
Center-crossing
Faster evolution? Better walkers?
D
Structure
Modular vs. fully connected, module size, interneurons
E
Time
What do evolved time constants do? Speed the circuit up
F
Robustness
A broken leg, noisy sensors, a push, a longer walk
G
Diversity
Same gait, same frequency, every seed?
H
Fitness
Penalize effort; make skating impossible
I
Search
GA vs. CMA-ES; population size; mutation
J
No memory
A feedforward walker: what can't it do?
Or something completely different. Details in the README.

## Slide 36: Let's demo
Unit 6: one circuit, seed 3, random vs. center-crossing.
Then: evolve a walker, and watch it.