## Slide 1: Six-Legged Walker: Brains with Their Own Rhythm
ECE497 Evolutionary Robotics · Project 6
Checkpoint: TBA (in class)
Report and presentations: TBA

## Slide 2: Every brain so far has been a function
Projects 3–4
Feedforward network
Output depends only on the current input
No memory: same input, same output
Project 5
Feedforward + a clock
Rhythm handed in from outside, as sin and cos inputs
The brain only shapes it
Project 6
CTRNN
Internal state that changes in time
Makes its own rhythm, even with no input
Walking is rhythmic. Insects walk using central pattern generators: circuits of neurons that produce a rhythm on their own. Can evolution build one?

## Slide 3: The task: make six legs walk
An evolved CTRNN walking, seen from above, head to the right. Red dots: feet down.
Six legs; each one swings forward and back, and puts its foot down or lifts it
A planted foot pushes the body; a lifted one swings back into place
The body only moves while the planted feet hold it up: a stable tripod
Fitness: average forward speed
Nobody tells it how to walk. Evolution has to find a leg-timing pattern, and a brain that produces it

## Slide 4: The CTRNN
A neural network that is a dynamical system
1
2
3

## Slide 5: One neuron, one equation
τi dyi/dt = −yi + Σj wji oj + Ii oi = σ(yi + θi)
y
state
The neuron's internal activity. This is what carries over from one moment to the next.
τ
time constant
How fast the state responds. Bigger τ, slower neuron.
−y
leak
With no input, the state decays back toward 0.
Σ w o
recurrent input
Weighted outputs of every neuron, including itself. w can be + or −.
θ
bias
Shifts where the neuron turns on.
o = σ(·)
output
Sigmoid of state + bias: always between 0 and 1. I is an external input, e.g. a sensor.

## Slide 6: What the bias and the time constant do
θ moves the sigmoid left or right: a neuron with a large bias is on almost no matter what, a very negative one is off.
τ sets the speed: the same input, switched on at t = 0, reaches the same value, sooner or later.

## Slide 7: Neurons talk to each other, in loops
1
2
3
Any neuron can connect to any other, and to itself
Feedforward: activity flows one way, through each layer once. Same input, same output.
Recurrent: activity keeps circulating. What the network does now depends on what it was doing a moment ago.
That's what lets it remember, and make its own rhythm.
In the code
Weights[j][i] = connection from neuron j to neuron i
Input to every neuron at once:
Weights.T @ Outputs

## Slide 8: Simulating it: tiny steps forward in time
def step(self, dt):
netinput = self.Inputs + np.dot(self.Weights.T, self.Outputs)
self.States += dt * (self.invTimeConstants
* (-self.States + netinput))
self.Outputs = sigmoid(self.States + self.Biases)
Euler integration: y ← y + dt · dy/dt
Compute how fast every state is changing right now, take a small step in that direction, repeat
dt must be small compared to the smallest τ. Too big, and the simulation is wrong; bigger still (dt > 2τ) and it blows up
Unit 6: τ ≥ 0.1, dt = 0.01. Project 6: τ ≥ 1, dt = 0.1
The exact answer rises smoothly to 1. With bigger steps it overshoots; at dt = 2.2 it diverges.

## Slide 9: Unit 6: a CTRNN in 60 lines of NumPy
import ctrnn
nn = ctrnn.CTRNN(3) # 3 neurons
nn.randomizeParameters() # random w, θ, τ
nn.setCenterCrossing() # optional (later)
nn.initializeState(np.random.uniform(-1, 1, 3))
for t in range(steps):
nn.step(dt)
outputs[t] = nn.Outputs
ctrnn.py
The network: states, weights, biases, time constants, step(dt)
sim.py
Simulate one circuit; plot each neuron over time, and neuron 1 vs. neuron 2
exp.py
Simulate hundreds of circuits; count how many oscillate
PythonBasics/Unit6: the same pieces as Project 6's controller, with nothing else attached. No body, no inputs: just the dynamics.

## Slide 10: With no inputs at all, a CTRNN can...
Settle down
All activity dies into a fixed point and stays there. The most common outcome for a random circuit.
Oscillate
Activity repeats forever, with its own period: a rhythm nobody put in from outside.
They can also switch between several resting states, or behave chaotically. Which you get depends on the parameters, and sometimes on where you start.

## Slide 11: A two-neuron oscillator
1
2
−1
+1
2 turns 1 on; 1 turns 2 off; 2 off lets 1 fall; 1 off lets 2 rise... Each neuron excites itself (+4.5), so it tends to stay on or off; the cross connections keep pushing them over the edge. In output space the trajectory ends in a loop: a limit cycle.
sim.py with circuit = "oscillator" (θ = −2.75, −1.75; τ = 1)

## Slide 12: Center-crossing: put every neuron where it's sensitive
Random weights and biases push most neurons fully on or fully off. A saturated neuron ignores its inputs, so activity freezes
A neuron's input from the others always lies between the sum of its negative weights and the sum of its positive ones
Center-crossing: set each bias so the middle of that range lands on the steepest part of the sigmoid
θi = −Σj wji / 2
nn.setCenterCrossing() Mathayomchan & Beer (2002)

## Slide 13: Same weights and time constants, different biases
# sim.py
size = 3
seed = 3
circuit = "random"
# or "centercrossing"
Same seed: same weights and time constants, only the biases change
Random: neuron 2 is pinned at 0, the others freeze within a few time units
Center-crossing: all three neurons cycle, forever

## Slide 14: How common is rhythm?
exp.py
100 random circuits per size, each with random and with center-crossing biases
Throw away the first 100 time units; count it as rhythmic if a neuron keeps swinging (2+ full cycles)
Random: 0–4%. Center-crossing: up to 37%, and more with more neurons
Why does one neuron never oscillate?
About 1 minute. Change sizes, samples, or the parameter ranges, and run it again.

## Slide 15: Try it: Unit 6
# sim.py: change these, run it again
size = 3
duration = 100.0
dt = 0.01
circuit = "random"
seed = None
python3 sim.py
python3 exp.py
Seed 3: random vs. center-crossing, same weights
Oscillator: what changes if you flip the sign of one cross connection?
dt: make it bigger until the plots change. When, and why?
Size: what do 10 center-crossing neurons do?
Duration: some circuits take a long time to settle. How long is long enough?
Output space: a point, a loop, or a tangle?

## Slide 16: From Unit 6 to the walker
Same equations, now wired to a body
L1
L2
L3
R3
R2
R1

## Slide 17: The walker body
L1
L2
L3
R3
R2
R1
Top-down; head to the right. Orange: foot down (L1, R2, L3: a tripod)
Senses: each leg's angle (6 numbers)
Acts: forward, backward, and foot for each leg (18 numbers in [0, 1])
foot > 0.5: planted. A planted leg pushes the body; a lifted leg swings
Balance: the body moves only while the planted feet hold it up: 3 or more, on both sides, around its center
Fitness: average forward speed, at most 1.0

## Slide 18: Things to know about the simulator
0.1 s
per tick. One CTRNN step per tick of the body (dt = 0.1)
220 s
per episode: 2,200 ticks, each from random starting leg angles
3
episodes averaged for every fitness evaluation
1.0
maximum speed. Fitness near 0: the body never got off the ground
Setup: a fresh virtual environment, then pip install -r requirements.txt
NumPy, Matplotlib, PyTorch, EvoTorch; plus Gymnasium and MuJoCo for the optional part. No special Python version this time.
The physics is idealized: no mass, friction or contact forces. That's what makes it fast, and what the optional MuJoCo part is about.

## Slide 19: Same CTRNN, wired to a body
Unit 6
CTRNN.step(dt)
netinput = Inputs + W.T @ Outputs
States += dt/τ * (-States + netinput)
Outputs = sigmoid(States + Biases)
Project 6
WalkerCTRNNController.act(observation)
inputs = WS * angle[leg] # sensors in
netinput = inputs + W.T @ Outputs
States += dt/τ * (-States + netinput)
Outputs = sigmoid(States + Biases)
return Outputs[command_idx] # 18 actions out
18 command neurons: forward, backward, and foot for each leg. Their outputs are the actions
Sensors: each command neuron hears its own leg's angle, through an evolved weight WS
The genome: numbers in [0, 1], decoded to weights and biases in [−16, 16] and time constants in [1, 20]
reset_state() randomizes the states at the start of every episode; act() is one Euler step

## Slide 20: One leg circuit, copied six times
L1
L2
L3
R3
R2
R1
■ across the body (CBW) ■ along each side (ISW) ● fwd, bwd ● foot
Every leg runs the same 3-neuron circuit (same weights): like an insect's segmental ganglia
A few connections between neighboring legs, also shared
24 genes build an 18-neuron network
Genome (module size 3)
W
WS
CBW
ISW
τ
θ
--module_size adds free interneurons to every leg's circuit

## Slide 21: Or one big network: choosing a topology
--topology | Settings | Neurons | Genome | Weight sharing
modular | --module_size 3 (default) | 18 | 24 | yes
modular | --module_size 5 | 30 | 50 | yes
modular | --module_size 8 | 48 | 104 | yes
fully_connected | --interneurons 0 | 18 | 378 | no
fully_connected | --interneurons 6 | 24 | 642 | no
Fully connected: every connection is its own gene. Nothing is assumed about legs or symmetry, and the genome is 16× bigger
Bigger isn't free: more genes, same budget of evaluations

## Slide 22: Where does the rhythm come from?
--mode cpg
Central pattern generator
brain
body
Sensors off. The rhythm has to come from the circuit alone.
--mode rpg
Reflexive pattern generator
brain
body
Sensors on (default). The rhythm can come from the circuit, the body, or both.
--mode mpg
Mixed
brain
body
Episodes alternate between sensors off and on. Fitness is the average: it has to walk either way.
Beer & Gallagher (1992). Try a walker in the mode it wasn't evolved in: sim.py --mode cpg

## Slide 23: Center-crossing, in the walker
--center_crossing seeds the first generation with center-crossing biases (including the sensory and inter-leg weights)
Only the starting population: evolution can move the biases anywhere afterward
Center-crossing walked in 3 of 3 runs. Random biases got stuck skating in 2 of 3
But the fastest walker of all (0.92) came from random biases
Three runs is an anecdote, not an answer. How would you find out?

## Slide 24: Evolving it
Running, watching, and reading what evolution built

## Slide 25: Running it
# evolve a CTRNN (about 3 minutes on a 16-core laptop)
python evolve.py --controller ctrnn --center_crossing --seed 1 --verbose --vizperf \
--output walker.npy --fitness_output walker_fit.npz
# score it; then again with its sensors cut
python sim.py --controller ctrnn --genome walker.npy --scores
python sim.py --controller ctrnn --genome walker.npy --mode cpg --scores
# gait diagram, neuron outputs, and an animation
python sim.py --controller ctrnn --genome walker.npy --trace walk.dat
python visualize_walker.py walk.dat --out_prefix walk --topology modular --module_size 3
Pass sim.py the same controller settings you evolved with. --algorithm es swaps the GA for CMA-ES.
Save --output and --fitness_output for every run you might want to plot later.

## Slide 26: Reading a gait diagram
One row per leg. Black: foot down. White: swinging
Bottom: body speed. It drops to 0 whenever the planted feet stop holding it up
Look for the pattern: one or two legs lifted at a time, in a repeating order: a slow wave-like gait, not a tripod. It stumbles twice before it settles in

## Slide 27: Inside the circuit
Every neuron's output over time, one row per leg: forward, backward, foot
Which neurons oscillate? Which just follow along?
Same circuit on every leg, but different timing: where do the phase differences come from?
Cut the sensors, remove a neuron, freeze an output: what breaks?

## Slide 28: Two walkers, two sources of rhythm
The walker evolved with its sensors off (cpg, center-crossing): a steady rhythm, never stalls
Evolved in | Sensors on | Sensors off
rpg | 0.77 | 0.04
cpg | 0.03 | 0.61
Average speed, 5 episodes, run under each condition
Each walker only works the way it evolved
The rpg walker needs its sensors: its rhythm runs through the body
The cpg walker makes its own rhythm, and live sensory input throws it off
Could one walker do both? --mode mpg

## Slide 29: Watch out: walking vs. skating
Fitness 0.07, and it plateaued there
All six feet down, pushing: the body glides forward
Until the feet are dragged too far behind, and it's stuck for good
Easy to find, better than standing still, a dead end
A fitness number tells you how far, not how. Look at the gait.

## Slide 30: How long it takes
3 min
per run on a 16-core laptop (50 genomes × 100 generations)
15,000
episodes per run: 50 × 100 × 3, each 2,200 ticks of physics
0
GPUs needed: the cost is the physics loop, spread across CPU cores
Time a short run on your own machine first: --popsize 20 --gens 20
Fewer cores, proportionally longer. Start early, and let runs work while you analyze others
Evolution is stochastic: one run is an anecdote. Use --seed, and several seeds before you trust a conclusion

## Slide 31: Optional: real physics
Does a walker evolved here walk in MuJoCo?

## Slide 32: Same genome, more realistic physics
The walker from the previous slides, on the MuJoCo hexapod: it stays upright, but moves only about 1.2 units in 50 s.
 | walker.py | hexapod (MuJoCo)
Physics | idealized | mass, friction, contact
Senses | 6 leg angles | 35 values
Acts | 18 values in [0, 1] | 12 torques: sweep, lift
Time step | 0.1 s | 0.05 s
hexapod_bridge.py: sweep torque = forward − backward; foot sets a target lift angle
--timescale (CTRNN speed vs. body) and --lift_gain matter, and interact
Expect it to fail at first. That gap is the challenge

## Slide 33: The assignment
The most open-ended project yet
P1
P2
P3
P4
P5
P6
how much is up to you

## Slide 34: Two required parts, one optional
Required 1
Evolve a CTRNN that walks
Really walks: stepping, not skating
Show it: fitness, gait diagram, animation
Explain how it walks: what are the neurons doing? Where does the rhythm come from?
Required 2
An experiment of your own
Ask a question about this world
Predict, vary one thing, enough seeds
What did you learn?
Optional · +1 extra credit
Walk in MuJoCo
Transfer a walker to the realistic body
Close the gap any way you like
A careful attempt counts, even if it never walks
Any settings, any topology, any mode. Say what you chose, and why.
Checkpoint: TBA (Part 1, demo) Report due: TBA Presentations: TBA

## Slide 35: Ideas for your experiment
A
Where's the rhythm?
cpg vs. rpg vs. mpg. Cut a walker's sensors
B
Inside the circuit
Lesion neurons or connections. Does one leg oscillate alone?
C
Center-crossing
Faster evolution? Better walkers?
D
Structure
Modular vs. fully connected, module size, interneurons
E
Time
What do evolved time constants do? Speed the circuit up
F
Robustness
A broken leg, noisy sensors, a push, a longer walk
G
Diversity
Same gait, same frequency, every seed?
H
Fitness
Penalize effort; make skating impossible
I
Search
GA vs. CMA-ES; population size; mutation
J
No memory
A feedforward walker: what can't it do?
Or something completely different. Details in the README.

## Slide 36: Required reading
R6A
CTRNNs that walk
Beer, R. D., & Gallagher, J. C. (1992). Evolving dynamical neural networks for adaptive behavior. Adaptive Behavior, 1(1).
CTRNNs evolved to make a six-legged insect walk, with and without sensory feedback. This project's body, its leg circuits, and its CPG / RPG / MPG modes all come from here.
R6B
Thinking in dynamics
Beer, R. D. (1995). On the dynamics of small continuous-time recurrent neural networks. Adaptive Behavior, 3(4).
What one- and two-neuron CTRNNs can do, and why: fixed points, switches, oscillations. The best place to learn to read a CTRNN as a dynamical system.
Further reading in the README: center-crossing (Mathayomchan & Beer, 2002), model CPGs for walking (Chiel, Beer & Gallagher, 1999), and the reality gap (Jakobi et al., 1995).

## Slide 37: Let's demo
Unit 6: one circuit, seed 3, random vs. center-crossing.
Then: evolve a walker, and watch it.